ADA – 2001 Auto Voice Phone Dialer

ADA-2001 SPECIFICATIONS:

- Telephone Numbers: Store up to 4 numbers in EPROM for dialing voice phones, numeric and/or voice pagers. Numbers may be up to 50 digits long with multiple PAUSE segments.  A PAUSE is 2 seconds long & contains 1 digit.

- Two Input Channels (1-2): For dry contact or voltage operation may be programmed for:

- Exit Delay (0-199 seconds)

- Entry delay (0-199 seconds)

- NO or NC operation

- Momentary, continuous or disabled

- Program each input channel to dial any or all 4 numbers

- PBX (PABX)-same for all channels

- ATTEMPTS: Program up to 9 attempts.

Numbers are dialed from 1-9 times regardless if attempts to connect are successful or not.

- Message Repeat: Programmable 1-3 times.

- EPROM MEMORY: Voice messages, phone numbers and dialer status information remain stored even after total power failure.

- LCD NUMERIC DISPLAY: A two line by 16-character LCD panel is used to display program, test and status information.

- LISTEN – IN: The listen in feature can be initiated by the called party any time for a 60 second period.

- REMOTE SHUT OFF: While in the listen-in or two way mode the called party may terminate the dialing the dialing process and de-activate the channel by pressing “#” twice within 1 second.

- LINE SEIZURE: Internal switching relay and terminals are provided to allow for line seizure hookup of incoming telephone line.

Pp

POWER REQUIREMENTS:

- STANDBY POWER: A 9v battery may be used for up to 24 hours uninterrupted operation.

- AUX OUTPUT: AN open collector transistor circuit allows for external devices like sirens, relays, etc. to be activated when any of the 2 channels is active. Current is limited to 500 mA. Applied voltage must be less than 32 VDC.

- SUPPLY VOLTAGE: 24vdc – 32 vdc

- CURRENT:( OPERATE MODE-STANDBY) 28 mA typ.

- CURRENT: (OPERATE MODE-DIALING) 100mA max.

- OPERATING TEMPATURE: -18 to 55 deg C (0-130 deg F)

- DIMENSIONS: 6” x 4” x 1.5”

- WEIGHT: 8oz.

For a more complete viewing of all of our products as well as spec sheets, wiring diagrams, and ordering information and please visit our website at:

www.housingdevices.com

# Text boxes

ADA-2001

Automatic Voice\Pager Dialer

1

4

7

P

2

5

8

0

R

6

9

#

M

3